SFARC Zoom System Set-up	v.20230301

1. Set-up LED Light on Light Stand
2. Set-up PA Speaker on AV Tripod
3. Attach Fixed Audience USB Camera to PA Tripod
4. Attach Fixed Front USB Camera to PA Tripod
5. Set-up Projection Screen
6. Set-up Projector
7. Set-up Light Stand for PTZ Camera
8. Attach USB PTZ Camera with the connectors facing the Zoom AV table.
9. Open Front Panel of Zoom Rack Case
10. Remove USB Keyboard and Mouse Pad from the Front Cover (USB drive is stored with Velcro)
11. Remove the Mouse and Stream Deck from bottom Rack Shelf
12. Plug the Stream Deck USB into the Zoom PC Front Panel USB Port
13. Remove the two Handheld Microphones (in storage bags) from the top Rack Shelf
14. Open the Rear Panel of the Zoom Rack Case
15. Remove the two Wireless Microphone Antennas from the Rear Cover
16. Uncap the two BNC antenna ports on either side of the Zoom Rack Case
17. Attach a Wireless Microphone Antenna to each BNC port
18. Unroll the large umbilical cable between the Zoom Rack Case and the Projector / Camera
19. Connect an AC Power Strip to the umbilical cable near the projector
20. Connect the Projector and PTZ Camera AC power to the Power Strip
21. Connect the umbilical cable HDMI cable to the Projector HDMI IN Port
22. Connect the umbilical cable USB cable to the PTZ Camera
23. Plug the umbilical cable AC Plug into the Zoom Rack Case Power Strip
24. Plug the umbilical cable HDMI cable into the Zoom Rack Case rear Projector Port
25. Plug the umbilical cable USB cable into the Zoom Rack Case rear PTZ Cam Port
26. Plug the Fixed Front USB Camera cable into the Zoom Rack Case rear Front Cam Port
27. Plug the Fixed Audience USB Camera cable into the Zoom Rack Case rear Audience Cam Port
28. Unroll the small umbilical cable between the Zoom Rack Case and the PA Speaker
29. Plug the umbilical cable two XLR cables into the PA Speaker
30. Plug the umbilical cable AC plug into the PA Speaker
31. Plug the umbilical cable two XLR cables into the Zoom Rack Case rear XLR Audio Ports
32. Plug the umbilical cable AC plug into the Zoom Rack Case Power Strip
33. Switch On the Zoom Rack Case Power Strip
34. Connect a Source PC HDMI cable to the Zoom Rack Case rear PC Port
35. Plug the Source Computer PSU into the Zoom Rack Case Power Strip. Power On the PC
36. Place the LCD Monitor on top of the Zoom Rack Case.
37. Connect a short HDMI Jumper between the Monitor and the Zoom Rack Case rear Monitor Port
38. Connect the Monitor AC plug to the Zoom Rack Case Power Strip. Power On the Monitor
39. Power On the Zoom PC
40. Power On the Projector
41. Size, adjust keystone and focus of the Projector
42. Power On the PA Speaker
43. Test or replace batteries in the Wireless Microphones

SFARC Zoom System Operation

1. Launch PTZ Software
2. Launch OBS and Enable Virtual Output
3. Launch Zoom, Sign-in, Enable Audio Source - Virtual Audio Cable and Video Source – OBS
4. Set the Zoom Audio mode to Original
5. Speed Test the Network. (min. 3 Mbps up)
6. Change Date CG on the OBS Logo Slide
7. Preview and Take all video sources to Program Output to verify
8. Power On the Wireless Microphones and test audio levels
9. Test Source PC Audio
10. Delete Previous recordings from the Zoom PC Videos Folder
11. Make a test recording on OBS, and also check the Zoom Feed Video and Audio.
12. Playback the test recordings of the sources and Program feed. Check Audio and Video

If PowerPoint, run through all slides to pre-load and test for embedded media.

If a source is disconnected, OBS software may not detect unless the Zoom Computer is restarted.